## Slide 1: Electromagnetic Stirring of Liquid Metals
Yash Ganatra (10BME 1043)
Internal Guide : Dr. Jayasankar Variyar
External Guide: Dr. Pramod Kumar
(May 2014)

## Slide 2
“Science” behind semi-solid forming
Directional solidification → dendritic microstructure:
→ defects such as inhomogeneity, cracks, porosity….
“Fragmentation” or detachment of dendrites during solidification can lead to non-dendritic microstructure.
Experiments carried out at ESRF, Grenoble
Directional solidification (bottom cooled) of Al-20 wt.% alloy.
Detachment of dendrites can be enhanced by forced convection such as EM stirring
Fragmentation influences macrosegregation and microstructure

## Slide 3
Reheated billet can be used in a die-casting machine to produce near net-shape components.
“Science” behind semi-solid forming……cont.
Automotive, aerospace, defence, structural
SSF components:
increased strength
no porosity
no solidification shrinkage
thin wall sections
low machining costs
Detachment of dendrites observed by Synchrotron X-ray Imaging (Arnberg and Mathiesen, 2006, NTNU, Norway)

## Slide 4: Methods of producing non-dendritic microstructure
Intrusive methods
Mechanical stirring
  Impellors/Twin screw
  Drum Rollers
  Cooling slopes
Dendrite fragmentation methods
  Active methods
  Rely on Dendrite fragmentation due to forced convection
  Passive methods
No dendrite shear only suppress the growth and formation
Low superheat pouring
Addition of grain refiners and modifiers to generate equiaxed growth
Non-Intrusive methods
Ultrasonic vibrations Electromagnetic stirring

## Slide 5: Literature review
Most literature focus
Rheological behavior of semisolid slurries.
Post processing of semisolid billets into components.
Reheating, heat treatment, Alloy development etc. Microstructure characterization.
Mechanical property characterization.
(tensile strength, fracture toughness, compression tests)
Extensive research on generating non-dendritic microstructure
  mostly mechanical stirring
  Electromagnetic (EM) stirring (generally rotary types)
Linear EM stirring (LEMS) widely accepted as most effective
No Literature on EM stirring using LEMS

## Slide 6: Contribution
Development of
A-V formulation in FLUENT
Validating code for infinitely long cylindrical current carrying conductor
Validating code for square bar
Necessity for development of A-J formulation in FLUENT
Development of model of Linear Electromagnetic stirrer using ANSYS FLUENT
Bottom Up Approach for design
Development of A-J formulation in FLUENT
Validating code for a circular coil
Validating code for solenoid subject space and time varying current densities

## Slide 7: Contribution (contd.)
Modeling LEMS as a set of 3 coils
Modeling LEMS as a set of 6 coils
Foundation for design of LEMS
zP
rP
H(zP,rp)
L
IA
IAI
IB
IBI
IC
ICI
L/6
R
Current exit
Current entry
(a)
(b)
(a) Coil arrangement in a two pole in a LEMS. (b) Phasor notation of currents.

## Slide 8: Working Principle
The principle of working is similar to that of a linear induction motor. Electrically it is a two pole motor.
Circular Coils  Stator winding , Liquid Metal  Rotor
The coils are displaced in space by 120º. 3 phase currents
produce travelling magnetic field along axis of coil.
This varying field induces voltage in the molten metal in the tangential direction. The induced voltage establishes tangential eddy currents in the liquid metal.
The eddy current(tangential) in the liquid metal and the magnetic field(radial and axial) produce forces(axial and radial) in the liquid metal. These forces set the liquid metal into motion.

## Slide 9: EM stirring- How it works ??
Solenoid coil
Jp(A/m)
H(z,r)
L
R
z
r
Field space
E is the electric field V/m
B is the magnetic flux density Wb/m2
H is the magnetic field intensity A/m
J is the current density A/m2
 is the permeability of the metal H/m
 is the conductivity S/m
v is velocity of the fluid m/s
Orientation and direction of primary current
Key parameters in generating the forces in desired direction.
Metals -electrically conducting
Induced currents, magnetic fields  Lorentz Force
Applications
grain refinement.
Mix immiscible liquid metals
Advantages
Non intrusive i No contamination.
Current and frequency i Control of stirring intensity, process.
Solenoid excited by an alternating current
Notes: A sinusoidal distribution of mmf along the axis of the coils is achieved when the coils are displaced in space by 120. When these space displaced coils are excited by three phase currents, the resulting mmf is sinusoidally distributed in space as well as time.

## Slide 11: Field Formulation (A-V)
: Magnetic Vector Potential
from Faraday’s Law
V: Electric scalar potential
or
(when velocities are not negligible)
,
(under Coulomb Gauge condition )
Assumptions:
a. Electro-neutrality ()
b. Quasi steady electromagnetic phenomena ( = 0)
c. Magnetostatic case or for axisymmetric AC arc ( = 0)

## Slide 12: Simplified Equation Set
FLUENT requires form of:
Unsteady Term
Flux Term
Diffusion Term
Source Term

## Slide 13: Validation 1 – Magnetic field around cylindrical current carrying conductor
 |  | Electric Potential (V) | Electrical Conductivity (S/m)
Copper | 1.26e-6 | High:670 Low:0 | 2700
Air | 1.26e-6 | 0 | 1e-5
 |  | Electric Potential (V) | Electrical Conductivity (S/m)
Copper | 1.26e-6 | High:670 Low:0 | 2700
Air | 1.26e-6 | 0 | 1e-5
 | A(V.s/m) | V (V)
Conductor_up | Zero normal gradient | 670
Conductor_down | Zero normal gradient | 0
Up | Zero normal gradient | Zero normal gradient
Down | Zero normal gradient | Zero normal gradient
Far_walls | Zero value | Zero normal gradient
Axis | Axis | Axis
Boundary Conditions
Material Properties
Geometry from 3D to 2D axisymmetric
Named Selections

## Slide 14: Results
(a)
(b)
(c)
(a): Line plot of magnetic field from FLUENT
(b): Comparison of line plots obtained from FLUENT and the analytical solution obtained in MATLAB
(c): Magnetic field inside the conductor

## Slide 15: Validation 2 – Magnetic field around current carrying bar
 | A (V.s/m) | V (V) | (S/m) | 
Conductor up | Zero Normal Gradient | 670 V | 2700 | 1.26e-6
Conductor down | Zero Normal Gradient | 0 V | 2700 | 1.26e-6
Up | Zero Normal Gradient | Zero Normal Gradient | 1e-5 | 1.26e-6
Down | Zero Normal Gradient | Zero Normal Gradient | 1e-5 | 1.26e-6
Front,Back,Left,Right (Far Walls) | Zero value | Zero Normal Gradient | 1e-5 | 1.26e-6
 | A (V.s/m) | V (V) |  | 
Conductor up | Zero Normal Gradient | 670 V | 2700 | 1.26e-6
Conductor down | Zero Normal Gradient | 0 V | 2700 | 1.26e-6
Up | Zero Normal Gradient | Zero Normal Gradient | 1e-5 | 1.26e-6
Down | Zero Normal Gradient | Zero Normal Gradient | 1e-5 | 1.26e-6
Front,Back,Left,Right (Far Walls) | Zero value | Zero Normal Gradient | 1e-5 | 1.26e-6
Geometry of bar
Line plot of magnetic field
along x at y=z=0
Boundary Conditions

## Slide 16
(a)
(b)
(c)
(a): Line plot of magnetic field inside the conductor
(b): Contour plot of Magnetic field from FLUENT
(c): Line plot of Current density magnitude along x at y=z=0

## Slide 17: Field Formulation (A-J)
In case of circular (closed) geometries, voltage cannot be given as the driving force.
A-J formulation  current density as driving force.

## Slide 18: Validation 3 – Magnetic field around current carrying coil
Inner radius (m) | Outer Radius (m) | Mean Radii (m) | Thickness (m) | Magnetic Permeability (Wb/m)
0.038 | 0.042 | 0.04 | 0.01 | 1.26 e-6
Coil Geometry
Geometric properties of coil
Hex mesh of coil
 | A (V.s/m)
Up | Zero Normal Gradient
Down | Zero Normal Gradient
Far Walls | Zero Normal Gradient
for -0.05<z<0.05
Boundary Conditions

## Slide 19
(a) Vectors of current density
(b) Axial Variation of Magnetic field strength
(c) Magnetic field vectors around a coil as seen
from top
(a)
(b)
(c)
Hr
Hz

## Slide 20: Validation 4 – Magnetic field around current carrying solenoid
Constant Current
Space Varying Current
Time Varying Current
Space and time varying current
Inner radius (m) | Outer Radius (m) | Mean Radii (m) | Thickness (m)
0.038 | 0.042 | 0.04 | 0.2
Solenoid Geometry
Geometric properties of solenoid
Inner radius (m) | Outer Radius (m) | Centre | Thickness (m) | Relative Magnetic Permeability of bar (Wb/m)
0.0 | 0.02 | (0.0,0.0,0.0) | 0.1 | 2000
Geometric properties of steel bar inside solenoid

## Slide 21: Solenoid – Constant Current
(b)
(a)
(a) Axial Variation of magnetic field strength
Hr
Hz
(b) Variation of Bz/Bo along
dimensionless quantity z/R
Hr < Hz
Hz constant along the axis
Hr prominent only at ends  end effects in a solenoid
Notes: End effects

## Slide 22: Solenoid Space Varying Current
(a)
(b)
(c)
Hz
Hr
Hz
Hz
Hr
L/R = 5
L/R = 10
L/R = 25
Notes: Increase in magnitude of Hz

## Slide 23: Solenoid -Time Varying current
(a)
(b)
(c)
Radial variation of Lorentz force magnitude
Radial variation of Fr
(c) Axial variation of Hz
Notes: F mag nearly equal to Fr mag

## Slide 24: Solenoid – Time Varying (contd)

## Slide 25: Solenoid – Space and Time Varying
(a)
(b)
(c)
Axial Variation of magnetic field strength at t= 1e-6 s
Axial Variation of magnetic field strength at t= 0.01 s
Axial Variation of magnetic field strength at t= 0.02 s
Hr
Hz
Hz
Hz
Hr

## Slide 26: Inferences
A space and time varying field is needed to generate Lorentz forces which cause stirring
A single phase space and time varying field creates Lorentz forces which vary in direction over one cycle.
Three phase currents are required to produce Lorentz forces which are in same direction over one cycle.

## Slide 27: Development of LEMS – 3 coils

## Slide 28: Design of LEMS – 6 coils

## Slide 29: Design of LEMS – 6 coils

## Slide 30: Generation of Axial force in LEMS

## Slide 31: Conclusions
Field formulation for electromagnetic problems
User Defined functions in ANSYS FLUENT to implement field formulations
Validating field formulations for simple electromagnetic problems
Design of Linear Electromagnetic Stirrer

## Slide 32: Scope
Modeling Magnetic Return Paths which concentrate flux lines insider the stirrer
Studying fluid flow in LEMS
Implementing Solidification and Melting module to study phase change

## Slide 33: Thank You!